Circuits Worksheet

In this circuit, R1 = R2.  I1 is the current flowing through R1, and I2 is the current flowing through R2.

Find algebraic expressions for the following quantities, in terms of R1,  R2 and (Vbat.

I1 =

I2 =

Itot =

Suppose we add another resistor in parallel (so we have three resistors in parallel, instead of two); we keep the same battery. Draw a diagram of this new circuit. Will Itot, the total current flowing through the battery, increase, decrease, or remain the same? Explain your answer.

Suppose we keep adding resistors in parallel. Will the total current increase, decrease, or remain the same?

Formulate a general rule for what happens to the total current flowing through the battery in a parallel circuit, when more resistors are added. How does this compare to the rule for what would happen when resistors are added to a series circuit?

The definition of the equivalent resistance of a circuit Requiv is:

When we add resistors in parallel, does the equivalent resistance of the circuit increase, decrease, or remain the same? Explain your answer. How does this compare to what happens when you add resistors to a series circuit?

In this circuit, R1 = R2 = R3 .

- Rank I1, I2 and I3 from largest to smallest: (largest) ____________________ (smallest).

What are the relative magnitudes of I1, I2 and I3; i.e.,

I2 / I 1  =   ______________?

I3 / I 1  =   ______________?

Explain your reasoning:

- Rank (V1, (V2, and (V3 from largest to smallest: (largest) ______________________ (smallest)

What are the relative magnitudes of (V1, (V2, and (V3; i.e.,

(V 2 / (V 1 =   ______________?

(V 3 / (V 1 =   ______________?

Explain:

- Write two separate algebraic expressions relating Itot (the current flowing through the battery) and I1, I2 and I3. (It is not necessary to use all three I’s in each equation.)

- Itot =

II.        Itot =

- Write two separate algebraic expressions relating (Vbat and (V1, (V2, and (V3. (It is not necessary to use all three (V’s in each equation.)

- (Vbat =

- (Vbat =

Now assume that R1 = R2 = R3 = 2 ohms, and that (Vbat = 12 V. Find the following values:

Hint: use your results from #2 and #4.

(V1 = _____________

(V2 = _____________

(V3 = _____________

- Find the following values:

I1 = _____________

I2 = _____________

I3 = _____________

Itot = _____________

- What is the equivalent resistance of the entire circuit? Explain how you got this.

- What is the equivalent resistance of the parallel combination (R1 and R2) alone? (That is, if that combination were hooked up to a battery by itself without R3, what would be its equivalent resistance? Explain your answer.

- Assume that the potential at the negative terminal of the battery is 0 volts. Write down the value of the potential at each point:

- _____

# _____

- _____

# _____

- _____

- _____

- Suppose the wire was cut at point C. What would happen to the current flowing through R1?

With the wire cut at point C, find these values:

(V3(with wire cut) = _____________

(V2(with wire cut) = _____________

10. Compared to the situation before the wire was cut, would there be an increase, a decrease, or no change in :

- the amount of current flowing through R1? Explain.

- the amount of current flowing through R3? Explain.

- the amount of current flowing through R2? Explain.

D. the amount of current flowing through the battery? Explain.

11. Suppose we go back to the original circuit (i.e., no cut in the wire at point C), and we add a third two-ohm resistor in parallel (to join R1 and R2).

Would the equivalent resistance of the parallel combination increase, decrease, or remain the same?

Would the equivalent resistance of the whole circuit increase, decrease, or remain the same? Explain your answer.

Would the amount of current flowing through the battery increase, decrease, or remain the same?

# Text boxes

R1

(Vbat

R2

R3

R1

(Vbat

#### A

R2

–

+

+

–

#### B

#### C

#### D

#### E

#### F

(

(

(

(

(

(