Physics 112

### Quiz #19

November 5, 1999

# Name: _______________________

IF YOU WANT A QUESTION GRADED OUT OF THREE POINTS (–1 [MINUS ONE] FOR WRONG ANSWER!!) WRITE “3” IN SPACE PROVIDED ON EACH QUESTION.

- Suppose that a continuous wire runs around the four edges of this page, carrying a clockwise current. Circle all letters corresponding to the directions of an external magnetic field that would not cause a torque to be exerted on this loop.

A.

B.

C.

D.

E.

F.

- Suppose you lower a large bar magnet on top of the loop described in #1, with the south pole of the magnet closer to the loop (i.e., long axis [N-S axis] of the magnet perpendicular to plane of loop). What should you expect to happen:

- Loop will be attracted toward the magnet.

- Loop will be repelled away from the magnet.

- Loop will be neither attracted nor repelled, but will experience a torque.

- Loop will experience no attraction, no repulsion, and no torque.

###### Grade out of 3? Write “3” here: _____

- A wire loop is sitting in a magnetic field. The field is pointing perpendicular to the plane of the loop. Which of these fields will cause the largest magnitude of current to flow in the loop?

- Initial value 10 T, constant

- Initial value 10 T, increasing at 2 T/s

- Initial value 5 T, decreasing at 3 T/s

- Initial value 20 T, constant

- Initial value 40 T, increasing at 1 T/s

###### Grade out of 3? Write “3” here: _____

- A uniform magnetic field points in the positive z direction; a straight wire carrying a current is sitting in this field. Rank in order the magnitude of the force exerted on this wire for the following five orientations of this wire:

- along the x axis

- along the y axis

- along the z axis

- in the xy plane, but not parallel to either the x or y axes

- in the yz plane, but not parallel to either the y or z axes

Answer: (largest)______________________________(smallest)     [Use “=” sign if necessary]

# Text boxes

(